## Slide 1: Dispersion Matching of Stable and Radioactive Beams
HST15, RCNP, Osaka
November 16-19, 2015
Georg P. Berg
University of Notre Dame
Joint Institute for Nuclear Astrophysics

## Slide 2
Outline
Dispersion matching in a nutshell
Brief summary of long history of dispersion matching
Dispersion matching at stable beam facilities
Dispersion matching at RI facilities

## Slide 3
Why do we dispersion match beam lines and spectrometers?
Resolution better than energy spread of accelerator, limited by resolving power of spectrometer D/(M*2x0)
Reconstruction of scattering angle target (fp) in dispersive plane (x); non-dispersive plane, angle (y), out-of-focus mode
What ion-optical parameters on target need to be “matched” to the
spectrometer?
Spacial Dispersion b16, for resolution
Angular dispersion b26, for target (fp) reconstruction
Focus on target b12=0, for k = dp/(d*p) = 0

## Slide 4: Spacial and Angular Dispersion Matching A Cartoon to Remember
b26 = (s21 s16 - s11 s26) C
Achromatic Beam
on Target
Dispersive Beam
on Target
Angular dispersion
on Target
b16 = - ¾ (1 + s11 s26 K - s21 s16K) ¾
s16 C
s11 T
Great diagnostic for beam
momentum distribution

## Slide 5: Defining a RAY
Ion-optical
element
Code TRANSPORT:
(x, Q, y, F, l, dp/p)
(1, 2, 3, 4, 5, 6 )
Convenient “easy to use” program
for beam lines with paraxial beams
Code: COSY Infinity:
(x, a, y, b, l, dK, dm, dz)
Needed for complex ion-optical systems including several
charge states
different masses
velocities (e.g. Wien Filter)
higher order corrections
Not defined in the figure are:
dK = dK/K = rel. energy
dm = dm/m = rel. mass
dz = dq/q = rel. charge change
a = px/p0
b = py/p0
All parameters are relative
to “central ray” properties
Not defined in the figure are:
dp/p = rel. momentum
l = beam pulse length
All parameters are relative
to “central ray”
central ray
Note: Notations in the Literature are not consistent!

## Slide 6: Transport of a ray
Ray at initial
Location 0
Ray after element at
Location t


6x6 Matrix
representing
optic element
(first order)

Note: We are not building “random” optical elements.
Many matrix elements = 0
because of symmetries, e.g. mid-plane symmetry

## Slide 7: Transport of a ray through a system of beam line elements
Ray at initial
Location 0
(e.g. a target)
Ray at final
Location n


6x6 Matrix
representing
first optic element
(usually a Drift)

xn = Rn Rn-1 … R0 x0
Complete system is represented by
one Matrix Rsystem = Rn Rn-1 … R0

## Slide 8: Dispersion Matching
High resolution experiments
Secondary beam (large dp/p)

## Slide 9: Solution of first order Transport and Complete Matching
For best Resolution in the
focal plane, minimize the
coefficients of all terms
in the expression of x f.p.
For best Angle Resolution
Minimize Coefficients of
d 0 in expression of U f.p.
Complete Matching
Note: Also the beam focus
b12 on target is important
(b12 = 0 for kinem. k = 0)
(1)
(2)
Spacial Dispersion Matching:
D.L. Hendrie In: J. Cerny, Editor,
Nuclear Spectroscopy and Reactions, Part A,
Academic Press, New York (1974), p. 365.
Hendrie, Dispersion Matching b16 = - — * —
D C
M T
D = s16 = Spectrometer dispersion
M = s11 = Spectrometer magnification

## Slide 10: Spacial and Angular Dispersion Matching
Solutions for b16 and b26 under conditions that
both d0-coefficients = 0 in (1) and (2)
s11 b16 T + s12 b26 + s16 C = 0
s21 b16 T + s22 b26 + s26 C = 0
b26 = (s21 s16 - s11 s26) C
b16 = - ¾ (1 + s11 s26 K - s21 s16K) ¾
s16 C
s11 T
Solutions:
(19)
(20)
Spacial Dispersion Matching
Angular Dispersion Matching
b12 = - ¾¾¾-
s12 b22
s11 T
(21)
Focusing Condition
= ¾¾¾-
s16 b22 K
s11 T

## Slide 11: Brief History of Dispersion matching
1956 Early spectrometers, MIT, ND (Browne-Buechner), effects on resolution
1974 D.L. Hendrie, - D*C/(M*T), target functions T,C, k defined and discussed
1978 Big Karl, disp. matched BL,ion-optics,insufficient diagn.,S. Martin, K. Brown
1986 K600, IUCF, Disp. Matching incl. angular dispersion, improved diagnostics, k>0 matching, 0 deg measurements, angle reconstruction.
1994, 1996 Study group to develop disp. Matching for GRAND RAIDEN (M. Fujiwara), lead: Y. Fujita, K. Hatanaka, T. Wakasa, T.Kawabata et al., H. Ejiri secured funds from Japanese government for fully dispersion matched WS course.
2000 Grand Raiden, developm. WS incl. all known effects and diagnostics, k=0 disp. matching. Resolv. Power limit of about p/dp =37000 at 300 – 400 MeV (p,p’)
Grand Raiden unique (one on this planet) high Resol. facility to study (GT fine structure with 20- 30 keV at 140 MeV/u, Yoshi Fujita, ( K600 E(3He) ~ 70Mev/u)
2008 K600, iThembaLABS (Ricky Smit, R. Neveling): Successful Int’l initiative (Japan (Hiro Fujita, Yoshi Fujita), Germany (P. von Neumann-Cosel, USA(GB) to implement dispersion matching incl. 0 deg measurements.
2006 T. Kawabata design of Matching for RI beam at BigRIPS/SHARAQ system.
> 2015 Future developments of High Energy Spectrometers at RI beam facilities,
e.g. FAIR, LEBS, H. Geissel, H.Weick, J. Winfield; FRIB, HRS, Remco, GB.

## Slide 12: BIG KARL Spectrometer (Juelich, KFZ)
Bending radius r0 = 1.98 m
Bmax = 1.7 T
Gap = 6cm
Weight = ~ 50 tons (D1)
~ 70 tons (D2)
Resolv. power: p/Dp = 0 - 20600
Dispersion = -2.0 to 26 cm/%
Magnification Mx = 0.63 – 1.26
Magnification My = 25.4 – 1.94
Large range: Emin /Emax = 1.14
Solid angle: < 12.5 msr

## Slide 13: BIG KARL Sample Spectra

## Slide 14: RCNP Facility Layout Osaka, Japan
Dispersion matched beam line WS to the high resolution spectrometer Grand Raiden
D = S16 = 17 cm/% = 17 m
M = S11 ~ - 0.45
Dispersion on target:
B16 = D/M = - 37 m
Resolving power:
2x0 = 1 mm
R = p/Dp = 37000

## Slide 15: Momentum and Angular Resolution
Spacial & Angular Dispersion Matching & Focus Condition allows
Energy Resolution: E/DE=23000, p/Dp = 40000, despite beam spread: E/DE = 1700 - 2500
Angular resolution: DUscatt = SQRT(DU2hor+DF2) = 4 - 8 msr
At angles close to beam (e.g. 0 deg) vert. angle
component is needed  Overfocus mode, small
target dimension, because (y|y) is large,
Limitation: multiple scattering in detector
Refs.: Y.Fujita et al, NIM B126(1997)274, H.Fujita et al. NIM A 469(2001)55, T.Wakasa et al, NIM A482(2002)79

## Slide 16: Grand Raiden High Resolution Spectrometer
Max. Magn. Rigidity: 5.1 Tm
Bending Radius r0: 3.0 m
Solid Angle: 3 msr
Resolv. Power p/dp 37000
Beam Line/Spectrometer fully matched
Dipole for in-
plane spin component
Faraday cup
for (3He,t)
Br(t) ~ 2*Br(3He)
←
IUCF
K600 !

## Slide 17: Diagnostic of Dispersion Matching
of beam line & spectrometer using a double strip target & multi slit
IUCF K600, 1986

## Slide 18: Grand Raiden Angle Calibration
Calibrated!
Data suggest: Use yfp not Ffp to calibrate angle!
Over-focus mode (b)

## Slide 19: Scattering Angle reconstructed from focal plane measurements using complete dispersion matching techniques
Q(target)
F(target)
E(3He) = 420 MeV

## Slide 20: Horizontal Beam Profiles in the Focal Plane of Grand Raiden
QM8U →Control lateral dispersion
QM9S →Control angular dispersion
Lateral and angular dispersions can be controlled independently
References
  Y. Fujita at al., NIMB 126(1997)274
  H. Fujita et al., NIMA 469(2001)55
  T. Wakasa et al., NIMA 482(2002)79
Dispersion matching for K = 0 with faint beam

## Slide 21: High Resolution Spectrometers Momentum Analysis
Momentum Resolving Power
Momentum Resolution:
For High Resolution using Spectrometers (no physical separation) consider the following
Momentum resolving power Rp has to meet the design goal (e.g. Grand Raiden: 37000, SHARAQ: 15000 for 2x0 = 1 mm), given by science requirements.
If beam momentum spread dp/p > 1/ Rp need Dispersion Matching or Beam Tracking, count rate limit ~106 p/sec, not suitable for high intensity stable beams.
RI beam with dp/p ~ 1- 3 % dispersion matched beam (-S16/S11) on target too large (50 –100 cm). Therefore, SHARAQ has several modes (achromatic, high resol. achromatic, dispersive)
RI beams, high energies, 100 – 300 MeV/A, tracking detectors in beam line (BigRips, SHARAQ)
Within limits (multiple-scattering in focal plane (FP) detectors) HO can be corrected using standard FP detectors (x,x’,y,y’).
(x|dp) = M16 = Momentum (p) dispersion
(x’|x) = M11 = Magnification
2x0 = Target spot size
Image size

## Slide 22: Dispersion matching modes
Beam momentum spread p/dp < Resolving power Rp: Full resolution without dispersion matching, beam line achromatic mode sufficient.
Beam momentum spread p/dp ~ (1- 10)* Rp: Full resolution requires dispersion matching, e.g. Grand Raiden: 300 MeV p: beam ~150 keV, resolution 13 keV, 400 MeV p: beam ~ 150 keV, resol. 17 keV
Secondary Radioactive Beam (RI) : Beam momentum spread p/dp > 10* Rp: Dispersion matching with full beam is possible but typically dispersed beam on target impractically large, e.g. SHARAQ: > 10 cm). Mitigation: Intermediate modes with reduced beam momentum spread/intensity or reduced resolution.

## Slide 23
SMART
Beam Factory RIBF at the RIKEN Accelerator Research Facility (RARF)
SHARAQ: Pionieering spectrometer in high resolution Dispersion Matching with RI beam.
BigRIPS: T. Kubo
Ion-optical design: T. Kawabata
Spectrometer: H. Sakai, T. Uesaka
Future projects under design:
FAIR, GSI: LEBS (Low energy buncher spectrometer)
FRIB, MSU: HRS (High rigidity spectrometer)

## Slide 26: Pair of Drift Chambers at Location H10

## Slide 27: SHARAQ, Modes of Operation
Beam line requires special design for high-resolution spectrometer measurements with RI-beams.
To achieve the high-resolution measurement with SHARAQ both dispersion matching and beam tracking methods are used.
Depending on experiments, the following modes are available
Dispersive
Mode
Achromatic
(large acceptance)
Resolution
Acceptance
Dp/p=1/15000
Dp/p=1/7500
Dp/p=1/1500
at target
Tracking at F6
Tracking at F5
Dp/p = +/- 0.3 %
Dqx= +/- 10 mr,
Dqy= +/- 30 mr
Dp/p = +/- 0.3 %
Dqx= +/- 10 mr,
Dqy= +/- 30 mr
Dp/p = +/- 2 %
Dqx= +/- 20 mr,
Dqy= +/- 20 mr
Achromatic
(high resolution)
Hor. Target spot : ~100 mm ~30 mm ~30 mm

## Slide 28
b16 = -14.76 m
b26 = 4.79 rad
Matching condition
T. Kawabata et. al.
NIM B 266 (2008).
b12 = 0, for k=dp/dq/p = 0

## Slide 29: “High resolution” achromatic mode
T. Kawabata
Dqx= +/- 10 mr, Dqy= +/- 30 mr, Dx = +/- 3 mm, Dy = +/- 3 mm, DP= +/- 0.3 %
F3
F4
F5
F6
FH7
FH8
FH9
target
Beam size < a few cm
Momentum acceptance is ± 0.3 %, keeping Dp/p of ~ 1/7500.
( F6)
1.56
0.00
1.36
0.00
0.64
0.00
0.00
0.74
0.00
0.36
same as diper. mode

## Slide 30: “Large acceptance” achromatic mode
Dqx= +/- 20 mr, Dqy= +/- 20 mr, Dx = +/- 3 mm, Dy = +/- 3 mm, DP= +/- 2 %
F4
F5
F6
F3
F-H7
F-H8
F-H9
target
Momentum acceptance
can be increase up to ± 2 %.
resolution Dp/p~1/1500 (at F5 )
Beam transport is different
from dispersion matching mode.
same as the standard BigRIPS
transport up to F5.

## Slide 31: Dispersion Matching of Beam Line and SHARAQ Spectrometer
250 MeV/u 14N beam, approx. 1000 events/s

## Slide 32: Resolution
Resolution: approx. 3.5 MeV
Resolution: approx. 0.65 MeV
Resolv. Power: 0.43 MeV

## Slide 33: End